## Slide 1
Acoustic Measurement Setup
Bhupatindra Malla, Ephraim Gutmark
University of Cincinnati

## Slide 2: Far-field Acoustic Measurements
ɸ = 90
ɸ = 0
Reflected
Side
ɸ = 180
Shielded
Side
Farfield Mic Array
Position
Upstream Angle
Downstream Angle
Flow
Direction
Expanding side
Nozzle Exit
Ramp(absent in baseline case)
 = 35
 = 150
 = 90
ɸ = 90
ɸ = 0
ɸ = 180
Azimuthal Angles
Ramp
11.25ft
Nozzle Centerline
Mic Num. |  (deg.)
1 | 35
2 | 40
3 | 50
4 | 60
5 | 70
6 | 80
7 | 90
8 | 100
9 | 110
10 | 120
11 | 130
12 | 140
13 | 150
Acquisition Frequency = 204.8kHz
Data File:
.mat format.
Contains variable “p” with pressure measurements.
Each column of data corresponds to one microphone.

## Slide 3
  Mics: ¼” B&K 4954 Free-field Condenser Mics
  Acquisition Frequency = 204.8kHz
  Linear array of 31 mics with 1” spacing between the mics
  Array is at 15 degrees angle to the non-expanding side of the nozzle.
  Array traverses perpendicular to the microphone array at steps of 1” for 20”.
Near-field Microphone Arrangement
1.5”
Mic Array on along ɸ = 0,
Minor axis plane
FLOW
15
Ramp(absent in
baseline case)
Nozzle Exit
1”
Traverse
Direction
1.5”
15
20”
30”
Near-field Microphone Grid
Y
X